## Slide 1: Parallel Programming Models

## Slide 2: History
Application Software
System
Software
SIMD
Message Passing
Shared Memory
Dataflow
Systolic
Arrays
Architecture
Uncertainty of direction paralyzed parallel software development!
Historically, parallel architectures tied to programming models
  Divergent architectures, with no predictable pattern of growth.

## Slide 3: Today
Extension of “computer architecture” to support communication and cooperation
  NEW: Communication Architecture
Defines
  Critical abstractions, boundaries, and primitives (interfaces)
  Organizational structures that implement interfaces (hw or sw)
Compilers, libraries and OS are important today

## Slide 4: Programming Model
What programmer uses in coding applications
Specifies communication and synchronization
Examples:
  Uniprocessor Sequential Programming
  Multiprogramming: no communication or synch. at program level
  Shared address space: like bulletin board
  Message passing: like letters or phone calls, explicit point to point
  Data parallel: more regimented, global actions on data
    Implemented with shared address space or message passing

## Slide 5: Fundamental Design Issues
Layered approach: contract between hardware/software
Programming model requirements:
  1 Naming: How are data and/or processes referenced?
  2 Operations: What operations are provided on these data?
  3 Ordering: How are accesses to data ordered and coordinated?
  4 Replication: How are data replicated to reduce communication?

## Slide 6: Sequential Programming Model
Contract:
  1. Naming: linear address space
  2. Operations: load/store
  3. Ordering: Program Order
  4. Replication: Cache memories
  Rely on dependencies on single location: dependence order
  Compiler/hardware violate other orders without getting caught
    e.g., Out-of-order execution!

## Slide 7: Shared Address Space (Shared Memory) Programming Model
1. Naming: Any process can name any variable in shared space
2. Operations: loads and stores, plus those needed for ordering
3. Simplest Ordering Model (Sequential Consistency) :
  Within a process/thread: sequential program order
  Across threads: some interleaving (as in time-sharing)
  Additional orders through synchronization
    Again, compilers/hardware can violate orders either:
      TRANSPARENTLY
      SPECIAL CONTRACT w/ SW: Relaxed Memory Consistency

## Slide 8: SAS Programming model (Cont.)
3. More on Ordering: Synchronization
  Mutual exclusion (locks)
    Ensure data access by only one process at a time
      Room that only one person can enter at a time
    No ordering guarantees among processes
  Event synchronization
    Ordering of events to preserve dependencies
      e.g., producer —> consumer of data
    3 main types:
      point-to-point: SIGNAL/WAIT, semaphores
      global: BARRIER
      group: group BARRIER

## Slide 9: SAS Programming model (Cont.)
4. Replication
  A load brings/replicates data transparently
  Hardware caches do this, e.g. in shared physical address space
  OS can do it at page level in shared virtual address space
  No explicit renaming, many copies one name: coherence problem

## Slide 10: Shared Address Space Architectures
Popularly known as shared memory machines or model
Any processor can directly reference any global memory location
  Communication occurs implicitly as result of loads and stores
Naturally provided on wide range of platforms
  History dates at least to precursors of mainframes in early 60s
    CPU + I/O processors
  Wide range of scale: few to hundreds of processors

## Slide 11: Shared Address Space Model
Process: virtual address space plus one or more threads of control
Portions of address spaces of processes are shared
  Writes to shared address visible to other threads (in other processes too)
  Natural extension of uniprocessors model: conventional memory operations for comm.; special atomic operations for synchronization
  OS uses shared memory to coordinate processes
S
t
o
r
e
P
1
P
2
P
n
P
0
L
o
a
d
P
0
p
r
i
v
a
t
e
P
1
p
r
i
v
a
t
e
P
2
p
r
i
v
a
t
e
P
n
p
r
i
v
a
t
e
Virtual address spaces for a
collection of processes communicating
via shared addresses
Machine physical address space
Shared portion
of address space
Private portion
of address space
Common physical
addresses

## Slide 12: Communication Hardware
Also natural extension of uniprocessor
Already have processor, one or more memory modules and I/O controllers connected by hardware interconnect of some sort
Memory capacity increased by adding modules, I/O by controllers
  Add processors for processing!
  For higher-throughput multiprogramming, or parallel programs

## Slide 13: History
“Mainframe” approach
  Motivated by multiprogramming
  Extends crossbar used for mem bw and I/O
  Originally processor cost limited to small
    later, cost of crossbar
  Bandwidth scales with p
  High incremental cost; use multistage instead
“Minicomputer” approach
  Almost all microprocessor systems have bus
  Motivated by multiprogramming, TP
  Used heavily for parallel computing
  Called symmetric multiprocessor (SMP)
  Latency larger than for uniprocessor
  Bus is bandwidth bottleneck
    caching is key: coherence problem
  Low incremental cost

## Slide 14: Example: Intel Pentium Pro Quad
  All coherence and multiprocessing glue in processor module
  Highly integrated, targeted at high volume
  Low latency and bandwidth

## Slide 15: Example: SUN Enterprise
  16 cards of either type: processors + memory, or I/O
  All memory accessed over bus, so symmetric
  Higher bandwidth, higher latency bus

## Slide 16: Scaling Up: UMA, NUMA, ccNUMA
  Problem is interconnect: cost (crossbar) or bandwidth (bus)
  Dance-hall: bandwidth still scalable, but lower cost than crossbar
    latencies to memory uniform (UMA), but uniformly large
  Distributed memory or non-uniform memory access (NUMA)
    Construct shared address space out of simple message transactions across a general-purpose network (e.g. read-request, read-response)
  Caching shared (particularly nonlocal) data: ccNUMA
“Dance hall”
Distributed memory

## Slide 17: Example: Cray T3E
  Scale up to 1024 processors, 480MB/s links
  Memory controller generates comm. request for nonlocal references
  NUMA but with NO CACHES
  No hardware mechanism for coherence (SGI Origin etc. provide this)

## Slide 18: Message Passing Programming Model
1. Naming: Processes can name private data directly.
  No shared address space
2. Operations: Explicit communication through send and receive
  Send data from private address space to another process
  Receive copies from process to private address space
  Must be able to name processes (sometimes TAG data)

## Slide 19: Message Passing Programming Model (cont.)
More on Naming and operations:
Can construct global address space on top of MP:
  program level (hashing)
  or translated by compiler (e.g., HPF), libraries or OS
  Example: Shared Virtual Memory (Kai Li, Princeton)
    Uses standard VIRTUAL address translation h/w: TLB, page tables
    Can provide SAS directly with little software support
    An unmapped address results in a page fault
    Message Passing transfers pages from node to node
    Remote node will provide the appropriate page

## Slide 20: Message Passing Programming Model (cont.)
3. Ordering:
  Program order within a process
  Send and receive can provide synch
  Mutual exclusion inherent
4. Replication:
  A receive replicates; subsequently use new name
  Replication is explicit in software above that interface

## Slide 21: Message Passing Architectures
Complete computer as building block, incl. I/O: Multicomputer
  Communication via explicit I/O operations
Programming model: directly access only private address space (local memory), comm. via explicit messages (send/receive)
High-level block diagram similar to distributed-memory SAS
  But comm. integrated at IO level, needn’t be into memory system
  Like networks of workstations (clusters), but tighter integration
  Easier to build than scalable SAS (less HW support required)
Programming model more removed from basic hardware operations
  Library or OS intervention

## Slide 22: Message-Passing Abstraction
  Send specifies buffer to be transmitted and receiving process
  Recv specifies sending process and application storage to receive into
  Memory to memory copy, but need to name processes
  Optional tag on send and matching rule on receive
  User process names local data and entities in process/tag space too
  In simplest form, the send/recv match achieves pairwise synch event
    Other variants too
  Many overheads: copying, buffer management, protection
Pr
ocess
P
Pr
ocess
Q
Addr
ess
Y
Addr
ess
X
Send
X, Q, t
Receive
Y
,
P
,
t
Match
Local pr
ocess
addr
ess space
Local pr
ocess
addr
ess space

## Slide 23: Evolution of Message-Passing Machines
Early machines: FIFO on each link
  Hw close to prog. Model; synchronous ops
  Replaced by DMA, enabling non-blocking ops
    Buffered by system at destination until recv
Topology was very important to MP arch.
  Ring, k-ary n-cube, Hypercube, Mesh
  Neighbor to neighbor communication
  Store&forward routing
  Topology dependent MP algorithms
Diminishing role of topology
  Introduction of pipelined routing
  Simplifies programming: all nodes at about same distance

## Slide 24: Example: IBM SP-2
  Made out of essentially complete RS6000 workstations
  Network interface integrated in I/O bus (bw limited by I/O bus)

## Slide 25: Example Intel Paragon

## Slide 26: Data Parallel Model
Programming model
  Operations performed in parallel on each element of data structure
  Logically single thread of control, performs sequential or parallel steps
  Conceptually, a processor associated with each data element
Architectural model
  Array of many simple, cheap processors with little memory each
    Processors don’t sequence through instructions
  Attached to a control processor that issues instructions
  Specialized and general communication, cheap global synchronization
Original motivations
  Matches simple differential equation solvers
  Centralize high cost of instruction fetch/sequencing

## Slide 27: Application of Data Parallelism
  Each PE contains an employee record with his/her salary
  If salary > 25K then
  salary = salary *1.05
  else
  salary = salary *1.10
  Logically, the whole operation is a single step
  Some processors enabled for arithmetic operation, others disabled
Other examples:
  Finite differences, linear algebra, ...
  Document searching, graphics, image processing, ...
Some machines:
  Thinking Machines CM-1, CM-2 (and CM-5)
  Maspar MP-1 and MP-2,

## Slide 28: Dataflow Architectures
Represent computation as a graph of essential dependencies
Ability to name operations, synchronization, dynamic scheduling
  Logical processor at each node, activated by availability of operands
  Message (tokens) carrying tag of next instruction sent to next processor
  Tag compared with others in matching store; match fires executionKey characteristics
1
b
a
+




c
e
d
f
Dataflow graph
f = a

d
Network
T
oken
stor
e
W
aiting
Matching
Instruction
fetch
Execute
T
oken queue
Form
token
Network
Network
Pr
ogram
stor
e
a = (b +1)

(b

c)
d = c

e
Manchester Dataflow

## Slide 29: Systolic Architectures
  Replace single processor with array of regular processing elements
  Orchestrate data flow for high throughput with less memory access
Different from pipelining
  Nonlinear array structure, multidirection data flow, each PE may have (small) local instruction and data memory
Different from SIMD: each PE may do something different
Represent algorithms directly by chips connected in regular pattern

## Slide 30: Systolic Arrays (contd.)
  Practical realizations (e.g. iWARP) use quite general processors
    Enable variety of algorithms on same hardware
  But dedicated interconnect channels
    Data transfer directly from register to register across channel
  Specialized, and same problems as SIMD
    General purpose systems work well for same algorithms (locality etc.)
y
(
i
) =
w
1

x
(
i
) +
w
2

x
(
i
+ 1) +
w
3

x
(
i
+ 2) +
w
4

x
(
i
+ 3)
x
8
y
3
y
2
y
1
x
7
x
6
x
5
x
4
x
3
w
4
x
2
x
w
x
1
w
3
w
2
w
1
x
in
y
in
x
out
y
out
x
out =
x
y
out =
y
in +
w

x
in
x
=
x
in
Example: Systolic array for 1-D convolution

## Slide 31: Toward Architectural Convergence
Evolution and role of software have blurred boundary
  Send/recv supported on SAS machines via buffers
  Can construct global address space on MP using hashing
  Page-based (or finer-grained) shared virtual memory
Hardware organization converging too
  Tighter NI integration even for MP (low-latency, high-bandwidth)
  At lower level, even hardware SAS passes hardware messages
Even clusters of workstations/SMPs are parallel systems
  Emergence of fast system area networks (SAN)
Programming models distinct, but organizations converging
  Nodes connected by general network and communication assists
  Implementations also converging, at least in high-end machines

## Slide 32: Data Parallel Convergence
Rigid control structure (SIMD in Flynn taxonomy)
  SISD = uniprocessor, MIMD = multiprocessor
Popular when cost savings of centralized sequencer high
  60s when CPU was a cabinet
  Replaced by vectors in mid-70s
    More flexible w.r.t. memory layout and easier to manage
  Revived in mid-80s when 32-bit datapath slices just fit on chip
  No longer true with modern microprocessors
Other reasons for demise
  Simple, regular applications have good locality, can do well anyway
  Loss of applicability due to hardwiring data parallelism
    MIMD machines as effective for data parallelism and more general
Prog. model converges with SPMD (single program multiple data)
  Contributes need for fast global synchronization
  Structured global address space, implemented with either SAS or MP

## Slide 33: Dataflow Convergence
Problems
  Operations have locality across them, useful to group together
  Handling complex data structures like arrays
  Complexity of matching store and memory units
  Expose too much parallelism (?)
Converged to use conventional processors and memory
  Support for large, dynamic set of threads to map to processors
  Typically shared address space as well:
  I-Structures provide synchronization
Lasting contributions:
  Integration of communication with thread (handler) generation
  Tightly integrated communication and fine-grained synchronization
  Remained useful concept for software (compilers etc.)

## Slide 34: Convergence: Generic Parallel Architecture
A generic modern multiprocessor
Node: processor(s), memory system, plus communication assist
  Network interface and communication controller
Scalable network
Convergence allows lots of innovation, now within framework
  Integration of assist with node, what operations, how efficiently...

## Slide 35: Parallel Programs
1. What are parallel programs
2. Programming for performance
  Parallel computing model
  Cost-effective computing
3. Workload-driven architectural evaluation
  Parallel programming scaling
Unlike sequential systems:
  can’t take workload for granted
  Software base not mature

## Slide 36: Classes of Applications
Characterized based on main data structures:
  Regular, e.g., arrays, vectors, etc.
  Irregular, e.g., graphs, trees, etc.
Irregular apps further classified based on communication:
  Regular patterns: perform same ops every iteration
  Irregular patterns: compute/communicate different items

## Slide 37: Motivating Problems
Scientific applications:
  Simulating Ocean Currents
  Simulating the Evolution of Galaxies
Scientific/commercial application:
  Rendering Scenes by Ray Tracing
Commercial application:
  Data Mining

## Slide 38: Simulating Ocean Currents
  Model as two-dimensional grids
  Discretize in space and time
    finer spatial and temporal resolution => greater accuracy
  Many different computations per time step
  Where is the parallelism?
    Grid element computation
Spatial discretization
Cross sections

## Slide 39: Simulating Galaxy Evolution
  Simulate the interactions of many stars evolving over time
  Computing forces is expensive
  O(n2) brute force approach
  Hierarchical Methods O(n log n) take advantage of force law:
  Where is the parallelism?
    Barnes-Hut approach: divide space in uneven sized cubes containing approx. same number of stars. Divide anew with star movement.
m1m2
G
r2
Star on which forces
are being computed
Star too close to
approximate
Small group far enough away
to approximate as a center of mass
Large group far
enough away to
approximate as
a center of mass

## Slide 40: Rendering Scenes by Ray Tracing
  Shoot rays into scene through pixels in image plane
  Follow their paths
    they bounce around as they strike objects
    they generate new rays: ray tree per input ray
  Result is color and opacity for that pixel
  Where is the parallelism?
    Computation per input ray

## Slide 41: Commercial Workload
  Data Mining: find relations, trends, associations in data
  Not queries
  Example: find associations among sets in transactions
    find itemsets of size k in transactions
    look for associations
  Where is the parallelism
    Creating itemsets of size k from itemsets k-1

## Slide 42: Creating a Parallel Program
Given a Sequential algorithm:
  Identify work to be done in parallel
  Partition work and data among processes
  Manage data access, communication and synchronization
Main goal: Speedup
Speedup (p) =
Performance(p)
Performance(1)
How much speedup is enough? Cost-effective Parallel Processing

## Slide 43: Steps in Creating a Parallel Program
Decomposition, Assignment, Orchestration, Mapping
  Programmer or system software (compiler, runtime, ...)
  Issues are the same
P
0
Tasks
Processes
Processors
P
1
P
2
P
3
p
0
p
1
p
2
p
3
p
0
p
1
p
2
p
3
Partitioning
Sequential
computation
Parallel
Program
A
s
s
i
g
n
m
e
n
t
D
e
c
o
m
p
o
s
i
t
i
o
n
M
a
p
p
i
n
g
O
r
c
h
e
s
t
r
a
t
i
o
n

## Slide 44: Decomposition
Break up computation into tasks
  Tasks may become available dynamically
  No. of available tasks may vary with time
Goal:
  Enough tasks to keep processes busy
  But not too many
  No. of tasks available => upper bound on achievable speedup

## Slide 45: Limited Concurrency: Amdahl’s Law
  What is it?
  Assume a 2-phase app: a sequential + parallel phase
  If fraction s of seq execution is inherently serial, speedup <= 1/s
  Speedup = lim < = 1/s
  Example app:
    sweep over n-by-n grid and do some independent computation
    sweep again and add each value to global sum
  What is time for first phase?
  What is time for second phase?
  Speedup = or at most 2
2n2
n2
p
+ n2
  How can you get better speedup?
1
1-s
p
+ s
p ->

## Slide 46: Pictorial Depiction
1
p
1
p
1
n2/p
n2
p
work done concurrently
n2
n2
Time
n2/p
n2/p
(c)
(b)
(a)

## Slide 47: Assignment
How do you assign work to processes?
  E.g. mechanism to make process compute forces on given stars
  Together with decomposition, also called partitioning
Structured approaches usually work well
  Code inspection (parallel loops) or understanding of application
  Static versus dynamic assignment
Static:
  Divide work evenly, statically, among P processes
  Load balancing: divide work not number of tasks
Dynamic:
  Process grabs a piece of work from a Work Queue and executes
  May put more work back to the queue
  Automatic load balancing: everyone keeps busy
  Work Queue: point of contention

## Slide 48: Orchestration
What is it?
  Naming data
  Structuring communication
  Synchronization
  Scheduling tasks
Goals:
  Reduce communication and synchronization cost
  Preserve locality of data reference
  Schedule tasks to satisfy dependencies early
  Reduce overhead of parallelism management
Architecture should provide efficient primitives

## Slide 49: Mapping
Which process runs on which particular processor?
  mapping to a network topology
One extreme: space-sharing
  Machine divided into subsets, only one app at a time in a subset
  Processes can be pinned to processors, or left to OS
Also common: time-sharing
Can leave resource management control to OS
  OS uses the performance techniques we will discuss later
Usually adopt the view: process <-> processor

## Slide 50: Parallelizing Computation vs Data
So far we focused on partitioning computation!
Partitioning Data is often a natural view too
  Computation follows data: owner computes
  Grid example; data mining; High Performance Fortran (HPF)
But not general enough
  Distinction between comp. and data often strong
    Barnes-Hut, Raytrace
  Retain computation-centric view
  Data access and communication is part of orchestration

## Slide 51: Example: Sequential Ocean
main() Solve(float **A)
begin begin
read(n); while (!done)
A = malloc(n * n); diff = 0;
initialize(A); for i=1 to n do
Solve(A); for j = 1 to n do
end main temp = A(i,j);
A(i,j)=0.2*(A(i,j)+A(i,j-1)+A(i,j+1)+A(i+1,j)+
A(i-1,j));
diff += abs(A(i,j) - temp);
end for
end for
if (diff / (n*n) < TOL) then done = 1;
end while
end Solve

## Slide 52: Example: SAS Parallel Ocean
main() Solve(float **A)
begin begin
p = NUM_PROCS(); pid = MY_PROC();
start_row = 1 + (pid + n/p);
end_row = start_row + n/p -1;
read(n); while (!done)
A = G_MALLOC(n * n); mydiff = diff = 0;
initialize(A); BARRIER();
CREATE(p); for i=start_row to end_row do
Solve(A); for j = 1 to n do
WAIT_FOR_END(p-1); temp = A(i,j);
end main A(i,j)=0.2*(A(i,j)+A(i,j-1)+A(i,j+1)+A(i+1,j)+
A(i-1,j));
mydiff += abs(A(i,j) - temp);
end for
end for
LOCK(dlock); diff += mydiff; UNLOCK(dlock);
BARRIER();
if (diff / (n*n) < TOL) then done = 1;
end while
end Solve

## Slide 53: Example: MP Parallel Ocean
main() Solve()
begin begin
p = NUM_PROCS(); pid = MY_PROC();
initialize(myA);
CREATE(p); while (!done)
Solve(); mydiff = diff = 0;
WAIT FOR END(p-1) SEND(border rows); RECEIVE(border rows);
end main for i=1 to n/p_do
for j=1 to n/p do
temp = myA(i,j);
myA(i,j)= ...
mydiff += abs(myA(i,j) - temp);
end for
end for
if(pid!=0)SEND(mydiff to 0);RECEIVE(done);
if(pid==0)
for i=1 to p-1 do diff += RECEIVE(mydiff)
if (diff / (n*n) < TOL) then done = 1;
BROADCAST(done);
end while
end Solve

## Slide 54: Workload-driven Evaluation in Uniprocessors
Decisions made only after quantitative evaluation
Measurements and technology lead to proposed features
Simulation
  Simulator to accurately model a feature of interest
  Workload run through the simulator to obtain results
  Together with cost and complexity lead to design

## Slide 55: Difficult Enough for Uniprocessors
Workloads need to be renewed and reconsidered
Accurate simulators costly to develop and verify
Simulation is time-consuming
But leads to good evaluation and design
Quantitative evaluation also important for multiprocessors
  Maturity of architecture, and continuity among generations
Good evaluation is critical, and we must learn to do it right

## Slide 56: More Difficult for Multiprocessors
What is a representative workload?
Software model has not stabilized
Many architectural and application degrees of freedom
  Impact of these parameters and their interactions can be huge
  High cost of communication
What are the appropriate metrics?
Simulation is expensive
  Realistic configurations and sensitivity analysis difficult
  Larger design space, but more difficult to cover
Understanding parallel programs as workloads is critical

## Slide 57: A Lot Depends on Sizes
Application and no. of procs affect inherent properties
  Load balance, communication, extra work, locality
  Communication to Computation ratio increases -> speedup decreases
























1
4
7
10
13
16
19
22
25
28
31
0
5
10
15
20
25
30
Number of processors
Number of processors
Speedup
Speedup

N
= 130

N
= 258

N
= 514

N
= 1,026































1
4
7
10
13
16
19
22
25
28
31
0
5
10
15
20
25
30

Origin—16 K

Origin—64 K

Origin—512 K

Challenge—16 K

Challenge—512 K

## Slide 58: Scaling: Why Worry?
Fixed problem size is limited
Too small a problem:
  May be appropriate for small machine
  Parallelism overheads dominate benefits for larger machines
    Load imbalance
    Communication to computation ratio
  May even achieve slowdowns
  Doesn’t reflect real usage, and inappropriate for large machines
    Can exaggerate benefits of architectural improvements
Too large a problem
  Difficult to measure improvement (next)

## Slide 59: Too Large a Problem
Suppose problem realistically large for big machine
May not “fit” in small machine
  Can’t run
  Thrashing to disk
  Working set doesn’t fit in cache
Fits at some p, leading to superlinear speedup
Real effect, but doesn’t help evaluate effectiveness
Users want to scale problems as machines grow

## Slide 60: Demonstrating Scaling Problems
Small & big Ocean problems on SGI Origin2000
Number of processors
Number of processors
Speedup
Speedup












1
3
5
7
9
1
1
1
3
1
5
1
7
1
9
2
1
2
3
2
5
2
7
2
9
3
1
0
5
10
15
20
25
30

Ideal

Ocean: 258 x 258














1
3
5
7
9
1
1
1
3
1
5
1
7
19
2
1
23
25
27
2
9
3
1
0
5
10
15
20
25
30
35
40
45
50

Ocean: 12 K x 12 K

Ideal

## Slide 61: Questions in Scaling
Under what constraints to scale the application?
  appropriate performance improvement metrics
How should the application be scaled?
Definitions:
  Scaling a machine: Can scale power in many ways
    Assume adding identical nodes, each bringing memory
  Problem size: Vector of input parameters, e.g. N = (n, q, t)
    Determines work done
    Distinct from memory usage
    Start by assuming it’s only one parameter n, for simplicity

## Slide 62: Under What Constraints to Scale?
Two types of constraints:
  User-oriented, e.g. particles, rows, transactions, I/Os per proc
  Resource-oriented, e.g. memory, time
Which is more appropriate depends on application domain
  User-oriented easier for user to think about and change
  Resource-oriented more general, and often more real
Resource-oriented scaling models:
  Problem constrained (PC)
  Memory constrained (MC)
  Time constrained (TC)

## Slide 63: Problem Constrained Scaling
User wants to solve same problem, only faster
  Video compression
  Computer graphics
  VLSI routing
But limited when evaluating larger machines
  SpeedupPC(p) =
Time(1)
Time(p)

## Slide 64: Time Constrained Scaling
Execution time is kept fixed as system scales
  User has fixed time to use machine or wait for result
Performance = Work/Time as usual, and time is fixed, so
  SpeedupTC(p) =
How to measure work?
  Execution time on a single processor?
  Should be easy to measure, ideally analytical and intuitive
  Should scale linearly with sequential complexity
  Can measure time with ideal memory system on a uniprocessor
Work(p)
Work(1)

## Slide 65: Memory Constrained Scaling
Scale so memory usage per processor stays fixed
Scaled Speedup: Is Time(1) / Time(p)?
  SpeedupMC(p) =
Can lead to large increases in execution time
  If work grows faster than linearly in memory usage
  e.g. matrix factorization: n x n, O(n2) mem, O(n3)
    10,000-by 10,000 matrix takes 800MB and 1 hour on uniprocessor
    With 1,000 processors, can run 320K-by-320K matrix
    but ideal parallel time (perfect speedup) grows to 32 hours!
Work(p)
Time(p)
x
Time(1)
Work(1)
=
Increase in Work
Increase in Time

## Slide 66: Cost-effective Parallel Processing
What speedup is acceptable ?
A: speedup(p) > costup(p)
  costup = cost(p) / cost(1)
  cost-performance = cost / performance = cost / (work/time)
Parallel computing is more cost-effective when:
  cost-performance(p) <= cost-performance(1) !
True when memory cost dominates!
  Even small speedups are cost-effective then!

## Slide 67: Taxonomy
Flynn’s taxonomy:
Programming model taxonomy:
  Shared-Memory, Message-passing, Dataflow, Systolic Array
Memory access taxonomy for Shared-Memory:
  UMA, NUMA, ccNUMA