## Slide 1: Bus-Based Multiprocessor
Most common form of multiprocessor!
Small to medium-scale servers: 4-32 processors
E.g., Intel/DELL Pentium II, Sun UltraEnterprise 450
Memory Bus
P
$
P
$
P
$
……..
Memory
A.k.a SMP or Snoopy-Bus Architecture

## Slide 2: Shared Cache Multiprocessor
Very small number of processors: up to 4
E.g., Dual-cpu Intel, Stanford Hydra on-chip multiprocessor
P
P
P
……..
Memory
Interleaved $
Interconnect

## Slide 3: Dance Hall Multiprocessor
Large-scale machines
E.g., NYU Ultracomputer, IBM RP3
P
$
P
$
P
$
……..
Memory
Memory
Interconnect

## Slide 4: Distributed Shared Memory (DSM)
Most common form of large shared memory
E.g., SGI Origin, Sequent NUMA-Q, Convex Exemplar
……..
Memory
Interconnect
Memory
Memory
P
$
P
$
P
$

## Slide 5: Cache Coherence Problem
P1
$
P2
$
X = 0
Load X
Store 4, X
Load X
Load X
Time
What value of X is in P1 and P2’s caches?
What value of X is in memory?

## Slide 6: Cache-coherence problem
X=0
X=0
X=1
X=0
X=0
Ld X
St X, 1
Ld X
...
Ld X
Memory
Cache0
Cache1
Proc0
Proc1
1
6
5
4
3
2
7
8

## Slide 7: Write-through Coherence Protocol
Memory
Cache0
Cache1
Proc0
Proc1
Ld X
1
X=0
4
X=0
2
Ld X
7
8
X=1
X=1
6
X=0
5a Write X
5c
X=1
5b
X=0
0
5
St X, 1
3
Ld X

## Slide 8: Write-through State Transition Diagram
  PrRd, PrWr
  BusRd (go to memory get data)
  BurWr (write data to memory/invalidate cached copies)
I
V
PrRd/BusRd
PrRd/—
PrWr/BusWr
BusWr/—
Processor-initiated transactions
Transactions on the BUS
PrWr/BusWr

## Slide 9: Problem with Write-Through
High bandwidth requirements
  Every write from every processor goes to shared bus and memory
  Consider 200MHz, 1CPI processor, and 15% instrs. are 8-byte stores
  Each processor generates 30M stores or 240MB data per second
  1GB/s bus can support only about 4 processors without saturating
  Write-through especially unpopular for SMPs
Write-back caches absorb most writes as cache hits
  Write hits don’t go on bus
  But now how do we ensure write propagation and serialization?
  Need more sophisticated protocols: large design space
Solution?
Write-back-based protocols

## Slide 10: Design Space for Snooping Protocols
No need to change processor, main memory, cache …
  Extend cache controller and exploit bus (provides serialization)
Focus on protocols for write-back caches
Design space
  Invalidation versus Update-based protocols
    On write invalidate or update other copies
  Set of states
    Block OWNER:
      thus far data comes only from memory which is always updated
      owner is the one that is responsible for supplying data

## Slide 11: Invalidate versus Update
Basic question of program behavior
  Is a block written by one processor read by others before it is rewritten?
Invalidation:
  Yes => readers will take a miss
  No => multiple writes without additional traffic
    and clears out copies that won’t be used again
Update:
  Yes => readers will not miss if they had a copy previously
    single bus transaction to update all copies
  No => multiple useless updates, even to dead copies
Need to look at program behavior and hardware complexity
Invalidation protocols much more popular (more later)
  Some systems provide both, or even hybrid

## Slide 12: Basic MSI Writeback Inval. Protocol
States
  Invalid (I)
  Shared (S): one or more
  Dirty or Modified (M): one only
Processor Events:
  PrRd (read)
  PrWr (write)
Bus Transactions
  BusRd: asks for copy with no intent to modify
  BusRdX: asks for copy with intent to modify
  BusWB (shown as Flush later on): updates memory
Actions
  Update state, perform bus transaction, flush value onto bus

## Slide 13: MSI: Behavior
(1) Read hit: use local copy; no state change (states S or M)
(2) Read miss:
- if M copy exists, it is flushed onto the bus and memory;
all copies set to S
- otherwise, access memory; state set to S
(3) Write hit:
- if local copy is S; request exclusive copy; other copies are invalidated; local copy set to M
- if local copy M; just write locally; no state changes
(4) Write miss:
- generate read excl. request; all other copies are invalidated; if M copy exists it is flushed; set local state to M

## Slide 14: Simple MSI Protocol: SGI 4D
Write-invalidate for write-back caches
PrRd: Processor read (load)
PrWr: Processor write (store)
BusRd: ReadOnly copy due to a PrRd
BusRdX: Writable copy due to a PrWr
BusWB: Writing back a block
BusInv: Invalidate other copies
BusCache: Cache-to-cache block transfer
BusUpdate: One/Two word update

## Slide 15: Simple MSI Protocol: SGI 4D
I
S
M
I - Invalid
S - Shared
M - Modified
PrWr/BusRdX
BusRdX/BusWB
PrWr/BusRdX
BusRd/BusWB
BusRdX/-
PrRd/BusRd
PrRd/-BusRd/-
PrRd/-PrWr/-

## Slide 16: MSI:State Transition Diagram
PrRd/—
PrRd/—
PrWr/BusRdX
BusRd/—
PrWr/—
S
M
I
BusRdX/Flush
BusRdX/—
BusRd/Flush
PrWr/BusRdX
PrRd/BusRd

## Slide 17: Lower-level Protocol Choices
BusRd observed in M state: what transitition to make, S or I?
Depends on expectations of access patterns
  S: assumption that I’ll read again soon, rather than other will write
    good for mostly read data
    what about “migratory” data
      I read and write, then you read and write, then X reads and writes...
      better to go to I state, so I don’t have to be invalidated on your write
  Synapse transitioned to I state
  Sequent Symmetry and MIT Alewife use adaptive protocols
Choices can affect performance of memory system

## Slide 18: MESI (4-state) Invalidation Protocol
“Problem” with MSI protocol
  Read/modify (e.g., locks) is 2 bus xactions, even if no-one sharing
    e.g. even in sequential program
    BusRd (I->S) followed by BusRdX or BusUpgr (S->M)

## Slide 19: MESI (4-state) Invalidation Protocol
Add exclusive state: write locally without xaction, but not modified
  Main memory is up to date, so cache not necessarily owner
  States
    invalid
    exclusive or exclusive-clean (only this cache has copy, but not modified)
    shared (two or more caches may have copies)
    modified (dirty)
OWNER: Who is responsible for most uptodate copy: cache or memory
  I -> E on PrRd if no-one else has copy
    “needs” “shared” signal on bus: wired-or line asserted in response to BusRd
    Really way of knowing whether other copies exist

## Slide 20: MESI State Transition Diagram
BusRdX/Flush
PrWr/BusRdX
PrWr/BusRdX
  Same bus transactions as MSI
  Only diff, need for shared signal (BusRd(S) means other copies exist)
PrWr/—
BusRd/Flush
PrRd/
BusRdX/Flush
PrWr/—
PrRd/—
PrRd/—
BusRd/Flush

E
M
I
S
PrRd/—
BusRd(S)

BusRdX/Flush
BusRd/
Flush
PrRd/
BusRd (!S)

## Slide 21: Alternative Description of CC Protocols
Read MISS:
  read to non-existent, INVALID
  generates BUS transaction
Read HIT:
  read to any other state other than INVALID
  never generates BUS transaction
Write MISS:
  write to INVALID, Non-existent, or READ-ONLY (SHARED, …)
  generates BUS transaction
Write HIT
  write to READ-WRITE state (Modified,...)

## Slide 22: MESI: behavior
(1) Read hit: use local copy; no state change (can be S, M or E)
(2) Read miss:
- if no other copy exists get from memory; set local copy to E
- if E or S copies exist; get from memory (or the cache w/ E); set all copies to S
- if M copy exists; get that (could be via memory); set both copies to S

## Slide 23: MESI: behavior
(3) Write hit:
- if local copy in E or M state; write locally; set state to M
- if local copy in S; invalidate all other copies; set state to M
(4) Write miss:
- if no other copy; get from memory; set state to M
- if M copy exists; flush that copy; set state to M
- if E or S copies exist; invalidate them; set state to M

## Slide 24: Lower-level Protocol Choices
Who supplies data on miss when not in M state: memory or cache
Original, lllinois MESI: cache, since assumed faster than memory
  Cache-to-cache sharing
Not necessarily true in modern systems
  Intervening in another cache more expensive than getting from memory

## Slide 25: Lower-level Protocol Choices
Cache-to-cache sharing also adds complexity
  How does memory know it should supply data (must wait for caches)
  Selection algorithm if multiple caches have valid data
But valuable for cache-coherent machines with distributed memory
  May be cheaper to obtain from nearby cache than distant memory
  Especially when constructed out of SMP nodes (Stanford DASH)

## Slide 26: MOESI: behavior
As MESI but new state O=Owned
Have copy which could be shared but memory does not have the most up-to-date value
As in MESI but w/ these differences:
a Read miss than brings in a remote M copy forces the remote copy to O state
upon replacing an O copy it has to be treated as a dirty block
Why this? Reduces memory traffic

## Slide 27: Coherence protocols
And now for a little bit of history

## Slide 28: Write-Once (invalidation)
First to be described in the literature4 states: I, V, R(eserved), D(irty), global invalidate line
(1) Read Hit:: access from cache, no state change
(2) Read Miss: if another cache has DIRTY copy, it inhibits memory, writes the line back, and the requesting cache gets copy
Else, the line is loaded from memory
All caches with a copy set it VALID
(3) Write hit : if the line is DIRTY, write proceeds locally
If RESERVED, proceed locally and mark DIRTY
If VALID, write-through and mark RESERVED; other caches set state to INVALID
(4) Write Miss: like a read miss, the line is copied from memory or from a DIRTY copy; line marked DIRTY. All other caches invalidate copies

## Slide 29
Write-Once Protocol
R
D
I - Invalid V - Valid R - Reserved D - Dirty
PrWr/-
PrWr/BusWrOnce
PrRd/-PrWr/-
V
I
BusRdX/BusWB
BusRd/BusWB
BusRd/-
BusRdX/-
PrRd/-
PrRd/-
BusRd/-
BusWB/-
BusRdX/-
PrRd/BusRd
PrWr/BusRdX
Reserved: had copy, written once and no-one asked for it yet
BusWrOnce: BusRdX followed by BusWB

## Slide 30: Synapse (invalidation)
First bus-based protocol Implemented! (protocol like SGI 4D)
3 states: I, S, and D
Avoid global inhibit line: use a tag bit in memory; if set, memory not uptodate
(1) Read hit: access from cache; no state change
(2) Read miss:
  If another cache has a DIRTY copy,it supplies a nack, then writes back to memory, resets tag bit in memory and sets its local state to INVALID; then the requesting cache makes a second miss; the loaded line is set to VALID
  If block Shared, read from memory
(3) Write hit: if DIRTY, proceed locally; no state change
  if VALID, proceed like a write miss; including data transfer. There is no invalidation signal
(4) Write miss: like a read miss but all VALID copies are set invalid
  line’s tag in main memory is set

## Slide 31: Synapse Protocol
High overhead on misses, probably only of historical interest
I
S
D
I - Invalid
S - Shared
D - Dirty
PrWr/BusRdX
BusRdX/BusWB
PrWr/BusRdX
BusRd/BusWB
BusRdX/-
PrRd/BusRd
PrRd/-BusRd/-
PrRd/-PrWr/-

## Slide 32: Berkeley (invalidation)
Multiprocessor Workstation (SPUR): 4 states: I, S, D and SD (shared-dirty)
Uses the fourth state to optimize cache-to-cache transfers
(1) Read hit: use local copy; no state changes
(2) Read miss:
  If block Dirty or Shared-Dirty, transfer cache-to-cache; if DIRTY copy exists it’s changed to Shared-Dirty; local copy is marked Shared
  If block Shared, read from memory; mark Shared
(3) Write hit:
  On Dirty, use local copy
  On Shared-Dirty Invalidate other copies; mark local copy DIRTY
(4) Write miss:
  Copy comes from owner (shared-dirty or memory); local copy set to DIRTY; others INVALID

## Slide 33: Berkeley Protocol
I - Invalid S - Shared SD - Shared-Dirty D - Dirty
SD
D
PrWr/BusInv
PrRd/-PrWr/-
S
I
BusRdX/BusWB
BusRdX/-BusInv/-
PrRd/-
BusRd/BusCache
PrRd/BusRd
BusRdX/-
BusInv/-
PrWr/BusRdX
PrRd/-BusRd/-
BusRd/BusCache

## Slide 34: Illinois Protocol
Implemented in SGI multiprocessors
4 states: I, V, S, VE (valid exclusive, similar to MESI)
Missed data always comes from caches, bus SharedLine
(1) Read hit: blah blah
(2) Read miss:
  If block Dirty, transfer cache-to-cache, and write back; state to shared
  If block Shared, transfer cache-to-cache; set state to Shared
  If no cached copy get from mem; set state to Valid-Exclusive
(3) Write hit: local Dirty? Grab that no state changes
  local VE? State to Dirty
  local Shared? Invalidate all other copies; state to Dirty
(4) Write miss:
  Same as Read miss; local set to Dirty all others invalidated

## Slide 35: Illinois Protocol
VE
D
I - Invalid S - Shared VE - Valid-Exclusive D - Dirty
PrWr/-
PrRd/-PrWr/-
S
I
BusRdX/BusWB
BusRdX/-
PrRd/-
PrRd/BusRd
PrRd/-
BusRdX/-
BusInv/-
PrWr/BusRdX
PrRd/- BusRd/BusCache
PrRd/BusRd
PrWr/BusInv
BusRd/BusWB
BusRd/BusCache
PrRd/BusRd
PrRd/BusRd
PrWr/BusRdX

## Slide 36: Firefly write-back update protocol
Good performance when multiple processors are repeatedly reading and updating the same location
3 states: VALID-EXCLUSIVE, SHARED and DIRTY (similar to MES w/o I)
global shared line

## Slide 37: Firefly: behavior
(1) Read hit: access from cache; no state change
(2) Read miss: if another cache has copy they place it on the bus (multiple possible); set all copies to SHARED; if DIRTY exists it is written back to memory otherwise get from memory and set state to Valid-Exclusive
(3) Write hit: if local copy is DIRTY proceed locally
if local copy is VE proceed locally; state set to DIRTY
if local copy is SHARED; a write to memory is initiated; other caches pick up copy and set their state to SHARED; local copy is set to either VE or SHARED (if other copies exist)
(4) Write miss: like a read miss; local copy is set to SHARED if other copies exist in which case memory is updated also; if no other copies exist local copy is set to DIRTY

## Slide 38: Dragon Write-back Update Protocol
4 states
  Exclusive-clean or exclusive (E): I and memory have it
  Shared clean (Sc): I, others, and maybe memory, but I’m not owner
  Shared modified (Sm): I and others but not memory, and I’m the owner
    Sm and Sc can coexist in different caches, with only one Sm
  Modified or dirty (D): I and, no one else
No invalid state
  If in cache, cannot be invalid
  If not present in cache, can view as being in not-present or invalid state

## Slide 39: Dragon Write-back Update Protocol
New processor events: PrRdMiss, PrWrMiss
  Introduced to specify actions when block not present in cache
New bus transaction: BusUpd
  Broadcasts single word written on bus; updates other relevant caches

## Slide 40: Dragon: behavior
(1) Read hit: proceed locally; no state change
(2) Read miss: if another cache has a D or Sm copy, it supplies data and raises the SharedLine signal. Supplying cache sets its copy to Sm; local copy is set to Sc
if no D or Sm copies exist value comes from memory; Any cache with a copy (E or Sc) raises the SharedLine signal; local copy is set to Sc if SharedLine is raised otherwise is set to E
(3) Write hit: if local copy is D proceed locally; no state change
if local copy in E; proceed locally; state set to D
if local copy is Sm or Sc; delay write and initiate bus write; other caches get new data and update their local copies; they set their copies to Sc; local copy is set to Sm if other copies exist otherwise is set to D
(4) Write miss: like a read miss copy comes from cache with Sm or D copy otherwise from M; if other copies exist they are set to Sc; local copy is set to Sm if other copies exist or D if this is the only copy

## Slide 41: Dragon State Transition Diagram
E
Sc
Sm
M
PrWr/—
PrRd/—
PrRd/—
PrRd/—
PrRdMiss/BusRd(S)
PrRdMiss/BusRd(S)
PrWr/—
PrWrMiss/(BusRd(S); BusUpd)
PrWrMiss/BusRd(S)
PrWr/BusUpd(S)
PrWr/BusUpd(S)
BusRd/—
BusRd/Flush
PrRd/—
BusUpd/Update
BusUpd/Update
BusRd/Flush
PrWr/BusUpd(S)
PrWr/BusUpd(S)

## Slide 42: Cache Coherence & Mem Ordering
Cache coherence
  For a single memory location (address)
    Program order per process
    Value returned by read is the “latest” value written
    Write propagation: writes become visible to other processes
    Write serialization: all writes are seen by the same order by all processes
Memory Consistency:
  Order of operations on all memory locations (addresses):
  What order all memory accesses appear to happen
  Sequential consistency:
    as if all accesses (independent of location) happened in some serial order which is an interleaving of local, individual program orders for all addresses

## Slide 43: Implementing SC
Two kinds of requirements
  Program order
    memory operations issued by a process must appear to become visible (to others and itself) in program order
  Atomicity
    in the overall total order, one memory operation should appear to complete with respect to all processes before the next one is issued
    needed to guarantee that total order is consistent across processes
    tricky part is making writes atomic

## Slide 44: Memory Order: What Programmers Expect
Load/Store
Memory is accessed in program order & atomically
P
P
P
……..
Shared Memory

## Slide 45: Memory Accessing Order
What should be value of A printed?
P
P
A = 0 and flag = 0
While (flag = = 0);
print A;
A = 1;
flag = 1;

## Slide 46: Memory Accessing Order: The Reality
What causes A to print 0?
Out-of-order execution in the processor
Compiler re-ordering accessing
Shared-memory hardware: network, write buffers, etc.
How do you make sure the programmer gets what they want?
Change the programming interface: memory models
The programmer enforces order through annotations
What are the advantages/disadvantages?

## Slide 47: Write Atomicity
Write Atomicity: Position in total order at which a write appears to perform should be the same for all processes
  Nothing a process does after it has seen the new value produced by a write W should be visible to other processes until they too have seen W
  Transitivity implies A should print as 1 under SC
  Problem if P2 leaves loop, writes B, and P3 sees new B but old A (from its cache, say)
P
1
P
2
P
3
A=1;
while (A==0);
B=1;
while (B==0);
print A;

## Slide 48: Sufficient Conditions for SC
  Every process issues memory operations in program order
  After a write operation is issued, the issuing process waits for the write to complete before issuing its next operation
  After a read operation is issued, the issuing process waits for the read to complete, and for the write whose value is being returned by the read to complete, before issuing its next operation (provides write atomicity)
Sufficient, not necessary, conditions
Clearly, compilers should not reorder for SC, but they do!
  Loop transformations, register allocation (eliminates!)
Even if issued in order, hardware may violate for better performance
  Write buffers, out of order execution
Reason: uniprocessors care only about dependences to same location
  Makes the sufficient conditions very restrictive for performance

## Slide 49: Coherence?
A memory operation M2 is subsequent to a memory operation M1 if the operations are issued by the same processor and M2 follows M1 in program order.
Read is subsequent to write W if read generates bus xaction that follows that for W.
Write is subsequent to read or write M if M generates bus xaction and the xaction for the write follows that for M.
Write is subsequent to read if read does not generate a bus xaction and is not already separated from the write by another bus xaction.
R
W
R
R
R
R
R
R
R
R
W
R
R
R
R
R
R
R
P
0
:
P
1
:
P
2
:

## Slide 50: SC in Write-through Example
Provides SC, not just coherence
Extend arguments used for coherence
  Writes and read misses to all locations serialized by bus into bus order
  If read obtains value of write W, W guaranteed to have completed
    since it caused a bus transaction
  When write W is performed w.r.t. any processor, all previous writes in bus order have completed

## Slide 51: MSI:State Transition Diagram
PrRd/—
PrRd/—
PrWr/BusRdX
BusRd/—
PrWr/—
S
M
I
BusRdX/Flush
BusRdX/—
BusRd/Flush
PrWr/BusRdX
PrRd/BusRd

## Slide 52: Satisfying Coherence
Everything like VI simple write-back protocol except for:
  Writes that don’t appear on the bus:
    sequence of such writes between two bus xactions for the block must come from same processor, say P
    in serialization, the sequence appears between these two bus xactions
    reads by P will seem them in this order w.r.t. other bus transactions
    reads by other processors separated from sequence by a bus xaction, which places them in the serialized order w.r.t the writes
    so reads by all processors see writes in same order
R
W
R
R
R
R
R
R
R
W
R
R
R
R
W
R
P
0
:
P
1
:
P
2
:

## Slide 53: Write Serialization?
write on bus from Px
….
Write on bus from Py
Write hit (has to be from same proc)
local reads (Py)
read or write from Pz
other reads
- Bus serializes all bus writes
and reads
- local reads serialized w/ respect
those on bus
- local writes?

## Slide 54: Satisfying Sequential Consistency
  Bus imposes total order on bus xactions for all locations
  Between xactions, procs perform reads/writes locally in program order
  So any execution defines a natural partial order
    Mj subsequent to Mi if (I) follows in program order on same processor, (ii) Mj generates bus xaction that follows the memory operation for Mi