## Slide 1: Cache Coherence in Scalable Machines Overview

## Slide 2: Bus-Based Multiprocessor
Most common form of multiprocessor!
Small to medium-scale servers: 4-32 processors
E.g., Intel/DELL Pentium II, Sun UltraEnterprise 450
LIMITED BANDWIDTH
Memory Bus
P
$
P
$
P
$
……..
Memory
A.k.a SMP or Snoopy-Bus Architecture

## Slide 3: Distributed Shared Memory (DSM)
Most common form of large shared memory
E.g., SGI Origin, Sequent NUMA-Q, Convex Exemplar
SCALABLE BANDWIDTH
……..
Memory
Interconnect
Memory
Memory
P
$
P
$
P
$

## Slide 4: Scalable Cache Coherent Systems
Scalable, distributed memory plus coherent replication
Scalable distributed memory machines
  P-C-M nodes connected by network
  communication assist interprets network transactions, forms interface
Shared physical address space
  cache miss satisfied transparently from local or remote memory
Natural tendency of cache is to replicate
  but coherence?
  no broadcast medium to snoop on
Not only hardware latency/bw, but also protocol must scale

## Slide 5: What Must a Coherent System Do?
Provide set of states, state transition diagram, and actions
Manage coherence protocol
  (0) Determine when to invoke coherence protocol
  (a) Find source of info about state of line in other caches
    whether need to communicate with other cached copies
  (b) Find out where the other copies are
  (c) Communicate with those copies (inval/update)
(0) is done the same way on all systems
  state of the line is maintained in the cache
  protocol is invoked if an “access fault” occurs on the line
Different approaches distinguished by (a) to (c)

## Slide 6: Bus-based Coherence
All of (a), (b), (c) done through broadcast on bus
  faulting processor sends out a “search”
  others respond to the search probe and take necessary action
Could do it in scalable network too
  broadcast to all processors, and let them respond
Conceptually simple, but broadcast doesn’t scale with p
  on bus, bus bandwidth doesn’t scale
  on scalable network, every fault leads to at least p network transactions
Scalable coherence:
  can have same cache states and state transition diagram
  different mechanisms to manage protocol

## Slide 7: Scalable Approach #2: Directories
Every memory block has associated directory information
  keeps track of copies of cached blocks and their states
  on a miss, find directory entry, look it up, and communicate only with the nodes that have copies if necessary
  in scalable networks, comm. with directory and copies is throughnetwork transactions
Many alternatives for organizing directory information

## Slide 8: Scaling with No. of Processors
Scaling of memory and directory bandwidth provided
  • Centralized directory is bandwidth bottleneck, just like centralized memory
  • Distributed directories
Scaling of performance characteristics
  traffic: no. of network transactions each time protocol is invoked
  latency = no. of network transactions in critical path each time
Scaling of directory storage requirements
  Number of presence bits needed grows as the number of processors
How directory is organized affects all these, performance at a target scale, as well as coherence management issues

## Slide 9: Directory-Based Coherence
Directory Entries include
  pointer(s) to cached copies
  dirty/clean
Categories of pointers
  FULL MAP: N processors -> N pointers
  LIMITED: fixed number of pointers (usually small)
  CHAINED: link copies together, directory holds head of linked list

## Slide 10: Full-Map Directories
Directory: one bit per processor + dirty bit
  bits: presence or absence in processor’s cache
  dirty: only one cache has a dirty copy & it is owner
Cache line: valid and dirty

## Slide 11: Basic Operation of Full-Map
• k processors.
• With each cache-block in memory: k presence-bits, 1 dirty-bit
• With each cache-block in cache: 1 valid bit, and 1 dirty (owner) bit
• Read from main memory by processor i:
  • If dirty-bit OFF then { read from main memory; turn p[i] ON; }
  • if dirty-bit ON then { recall line from dirty proc (cache state to shared); update memory; turn dirty-bit OFF; turn p[i] ON; supply recalled data to i;}
• Write to main memory by processor i:
  • If dirty-bit OFF then { supply data to i; send invalidations to all caches that have the block; turn dirty-bit ON; turn p[i] ON; ... }
  • ...

## Slide 12: Example
P1
P2
P3
read x
read x
read x
C
data
x:
P1
P2
P3
write x
C
data
x:
data
data
data
P1
P2
P3
D
data
x:
data

## Slide 13: Example: Explanation
Data present in no caches
3 Processors read
P3 does a write
  C3 hits but has no write permission
  C3 makes write request; P3 stalls
  memory sends invalidate requests to C1 and C2
  C1 and C2 invalidate theirs line and ack memory
  memory receives ack, sets dirty, sends write permission to C3
  C3 writes cached copy and sets line dirty; P3 resumes
  P3 waits for ack to assure atomicity

## Slide 14: Full-Map Scalability (storage)
If N processors
Need N bits per memory line
Recall memory is also O(N)
O(NxN)
OK for MPs with a few 10s of processors
for larger N, # of pointers is the problem

## Slide 15: Limited Directories
Keep a fixed number of pointers per line
Allow number of processors to exceed number of pointers
Pointers explicitly identify sharers
  no bit vector
Q? What to do when sharers is > number of pointers
  EVICTION: invalidate one of existing copies to accommodate a new one
  works well when “worker-set” of sharers is just larger than # of pointers

## Slide 16: Limited Directories: Example
P1
P2
P3
read x
C
data
x:
data
data
P1
P2
P3
C
data
x:
data
data

## Slide 17: Limited Directories: Alternatives
What if system has broadcast capability?
  Instead of using EVICTION
  Resort to BROADCAST when # of sharers is > # of pointers

## Slide 18: Limited Directories
DiriX
  i = number of pointers
  X = broadcast/no broadcast (B/NB)
Pointers explicitly address caches
  include “broadcast” bit in directory entry
  broadcast when # of sharers is > # of pointers per line
DiriB works well when there are a lot of readers to same shared data; few updates
DiriNB works well when number of sharers is just larger than the number of pointers

## Slide 19: Limited Directories: Scalability
Memory is still O(N)
# of entries stays fixed
size of entry grows by O(lgN)
O(N x lgN)
Much better than Full-Directories
But, really depends on degree of sharing

## Slide 20: Chained Directories
Linked list-based
  linked list that passes through sharing caches
Example: SCI (Scalable Coherent Interface, IEEE standard)
N nodes
O(lgN) overhead in memory & CACHES

## Slide 21: Chained Directories: Example
read x
C
data
x:
P1
P2
P3
data
CT
C
data
x:
P1
P2
P3
data
CT
data

## Slide 22: Chained Dir: Line Replacements
What’s the concern?
  Say cache Ci wants to replace its line
  Need to breakoff the chain
Solution #1
  Invalidate all Ci+1 to CN
Solution #2
  Notify previous cache of next cache and splice out
  Need to keep info about previous cache
  Doubly-linked list
  extra directory pointers to transmit
  more memory required for directory links per cache line

## Slide 23: Chained Dir: Scalability
Pointer size grows with O(lg N)
Memory grows with O(N)
  one entry per cache line
  cache lines grow with O(N)
O(N x lg N)
Invalidation time grows with O(N)

## Slide 24: Cache Coherence in Scalable Machines Evaluation

## Slide 25: Review
Directory-Based Coherence
Directory Entries include
  pointer(s) to cached copies
  dirty/clean
Categories of pointers
  FULL MAP: N processors -> N pointers
  LIMITED: fixed number of pointers (usually small)
  CHAINED: link copies together, directory holds head of linked list

## Slide 26: Basic H/W DSM
Cache-Coherent NUMA (CCNUMA)
Distribute pages of memory over machine nodes
Home node for every memory page
Home directory maintains sharing information
Data is cached directly in processor caches
Home id is stored in global page table entry
Coherence at cache block granularity

## Slide 27: Basic H/W DSM (Cont.)
P
Cache
DSM NI
Memory
Dir
P
Cache
DSM NI
Memory
Dir
Network
Home Pages
Cached Data

## Slide 28: Allocating & Mapping Memory
  First you allocate global memory (G_MALLOC)
  As in Unix, basic allocator calls sbrk() (or shm_sbrk())
  Sbrk is a call to map a virtual page to a physical page
  In SMP, the page tables all reside in one physical memory
  In DSM, the page tables are all distributed
  Basic DSM => Static assignment of PTE’s to nodes based VA
  e.g., if base shm VA starts at 0x30000000 then
    first page 0x30000 goes to node 0
    second page 0x30001 goes to node 1

## Slide 29: Coherence Models
Caching only of private data
Dir1NB
Dir2NB
Dir4NB
Singly linked
Doubly linked
Full map
No coherence - as if all was not shared

## Slide 30: Results: P-thor

## Slide 31: Results: Weather & Speech

## Slide 32: Caching Useful?
Full-map vs. caching only of private data
  For the applications shown full-map is better
  Hence, caching considered beneficial
  However, for two applications (not shown)
  Full-map is worse than caching of private data only
    WHY? Network effects
    1. Message size smaller when no sharing is possible
    2. No reuse of shared data

## Slide 33: Limited Directory Performance
Factors:
  Amount of shared data
  # of processors
  method of synchronization
P-thor does pretty well
Others not:
  high-degree of sharing
  Naïve-synchronization: flag + counter (everyone goes for same addresses)
Limited much worse than Full-map

## Slide 34: Chained-Directory Performance
Writes cause sequential invalidation signals
Widely & Frequently Shared Data
  Close to full
Difference between Doubly and Singly linked is replacements
  No significant difference observed
  Doubly-linked better, but bot by much
    Worth the extra complexity and storage?
  Replacements rare in specific workload
Chained-Directories better than limited, often close to Full-map

## Slide 35: System-Level Optimizations
Problem: Widely and Frequently Shared Data
Example 1: Barriers in Weather
  naïve barriers:
    counter + flag
    Every node has to access each of them
    Increment counter and then spin on flag
    THRASHING in limited directories
Solution: Tree barrier
  Pair nodes up in Log N levels
  In level i,notify your neighboor
  Looks like a tree:)

## Slide 36: Tree-Barriers in Weather
Dir2NB and Dir4NB perform close to full
Dir1NB still not so good
  Suffers from other shared data accesses

## Slide 37: Read-Only Optimization in Speech
Two dominant structures which are read-only
Convert to private
At Block-level: not efficient (can’t identify whole structure)
At Word-level: as good as full

## Slide 38: Write-Once Optimization in Weather
Data written once in initialization
Convert to private by making a local, private copy
NOTE: EXECUTION TIME NOT UTILIZATION!!!

## Slide 39: Coarse Vector Schemes
Split the processors into groups, say r of them
Directory identifies group, not exact processor
When bit is set, messages need to be send to each group
DIRiCVr
good when number of sharers is large

## Slide 40: Sparse Directories
Who needs directory information for non-cached data?
Directory-entries NOT associated with each memory block
Instead, we have a DIRECTORY-CACHE

## Slide 41: Directory-Based Systems: Case Studies

## Slide 42: Roadmap
DASH system and prototype
SCI

## Slide 43: A Popular Middle Ground
Two-level “hierarchy”
Individual nodes are multiprocessors, connected non-hiearchically
  e.g. mesh of SMPs
Coherence across nodes is directory-based
  directory keeps track of nodes, not individual processors
Coherence within nodes is snooping or directory
  orthogonal, but needs a good interface of functionality
Examples:
  Convex Exemplar: directory-directory
  Sequent, Data General, HAL: directory-snoopy

## Slide 44: Example Two-level Hierarchies

## Slide 45: Advantages of Multiprocessor Nodes
Potential for cost and performance advantages
  amortization of node fixed costs over multiple processors
  can use commodity SMPs
  less nodes for directory to keep track of
  much communication may be contained within node (cheaper)
  nodes prefetch data for each other (fewer “remote” misses)
  combining of requests (like hierarchical, only two-level)
  can even share caches (overlapping of working sets)
  benefits depend on sharing pattern (and mapping)
    good for widely read-shared: e.g. tree data in Barnes-Hut
    good for nearest-neighbor, if properly mapped
    not so good for all-to-all communication

## Slide 46: Disadvantages of Coherent MP Nodes
Bandwidth shared among nodes
  all-to-all example
Bus increases latency to local memory
With coherence, typically wait for local snoop results before sending remote requests
Snoopy bus at remote node increases delays there too, increasing latency and reducing bandwidth
Overall, may hurt performance if sharing patterns don’t comply

## Slide 47: DASH
University Research System (Stanford)
Goal:
  Scalable shared memory system with cache coherence
Hierarchical System Organization
  Build on top of existing, commodity systems
Directory-based coherence
Release Consistency
Prototype built and operational

## Slide 48: System Organization
Processing Nodes
  Small bus-based MP
  Portion of shared memory
Processor
Cache
Processor
Cache
Memory
directory
Processor
Cache
Processor
Cache
Memory
directory
Interconnection Network

## Slide 49: System Organization
Clusters organized by 2D Mesh

## Slide 50: Cache Coherence
Invalidation protocol
Snooping within cluster
Directories among clusters
Full-map directories in prototype
  Total Directory Memory: P x P x M / L
  About 12.5% overhead
  Optimizations:
    Limited directories
    Sparse Directories/Directory Cache
    Degree of sharing: small, < 2 about 98%

## Slide 51: Cache Coherence: States
Uncached:
  not present in any cache
Shared:
  un-modified in one or more caches
Dirty:
  modified in only one cache (owner)

## Slide 52: Memory Hierarchy
4 levels of memory hierarchy

## Slide 53: Memory Hierarchy and CC, contd.
Snooping coherence within local cluster
  Local cluster provides data it has for reads
  Local cluster provides data it owns (dirty) for writes
  Directory info not changed in these cases
Accesses leaving cluster
  First consult home cluster
    This can be the same as local cluster
  Depending on state request may be transferred to a remote cluster

## Slide 54: Cache Coherence Operation: Reads
Processor Level:
  if present locally, supply locally
  Otherwise, go to local cluster
Local Cluster Level:
  if present in cache, supply locally; no state change
  Otherwise, go to home cluster level
Home Cluster Level:
  Looks at state and fetches line from main memory
  If block is clean, send data to requester/state changed to SHARED
  If block is dirty, forward request to remote cluster holding dirty data
Remote Cluster Level
  dirty cluster sends data to requester, marks copy shared and writes back a copy to home cluster level

## Slide 55: Cache Coherence Operation: Writes
Processor Level
  if dirty and present locally, write locally
  Otherwise, go to local cluster level
Local Cluster Level
  read exclusive request is made on local cluster bus
  if owned in a cluster cache, transfer to requester
  Otherwise, go to home cluster level
Home Cluster Level
  if present/uncached or shared, supply data and invalidate all other copies
  if present/dirty, read-exclusive request forwarded to remote dirty cluster
Remote Cluster Level
  if invalidate request is received, invalidate and ack (is shared)
  if rdX request is received, respond directly to requesting cluster and send dirty-transfer message to home cluster level indicating new owner of dirty block

## Slide 56: Consistency Model
Release Consistency
  requires completion of operations before a critical section is released
  “fence” operations to implement stronger consistency via software
Reads
  stall until read is performed (commercial CPU)
  read can bypass pending writes and releases (not acquires)
Writes
  write to buffer; stall if full
  can proceed when ownership is granted
  writes are overlapped

## Slide 57: Consistency Model
Acquire
  stall until acquire is performed
  can bypass pending writes and releases
Release
  send release to write buffer
  wait for all previous writes and releases

## Slide 58: Memory Access Optimizations
Prefetch
  Recall stall on reads
  software controlled
  non-binding prefetch
    second load at the actual place of use
  exclusive prefetch possible
    if know that will update
Special Instructions
  update-write
    simulate update protocol
    update all cached copies
  deliver
    update a set of clusters
    similar to multicast

## Slide 59: Memory Access Optimizations, contd.
Synchronization Support
Queue-based locks
  directory indicates which nodes are spining
  one is chosen at random and given lock
Fetch&Inc and Fetch&Dec for uncached locations
  Barriers
  Parallel Loops

## Slide 60: DASH Prototype - Cluster
4 MIPS R3000 Procs + Fp CoProcs /33Mhz
  SGI Powerstation motherboard really
64KB I + 64K D caches + 256KB unified L2
All direct-mapped and 16-line blocks
Illinois protocol (MESI) within cluster
MP Bus pipelined but not split-transaction
Masked retry “fakes” split transaction for remote requests
  Proc. is NACKed and has to retry request
Max bus bandwidth: 64Mbytes/sec

## Slide 61: DASH Prototype - Interconnect
Pair of meshes
  one for requests
  one for replies
16 bit wide channels
Wormhole routing
Deadlock avoidance
  reply messages can always be consumed
  independent request and reply networks
  nacks to break request-request deadlocks

## Slide 62: Directory Logic
Directory Controller Board (DC)
  directory is full-map (16-bits)
  initiates all outward bound network requests and replies
  contains X-dimension router
Reply Controller Board (RC)
  Receives and Buffers remote replies via remote access cache (RAC)
  Contains pseudo-CPU
    passes requests to cluster bus
  Contains Y-dimension router

## Slide 63: Example: Read to Remote/Dirty Block
a. CPU issues read on bus and
is forced to retry
RAC entry is allocated
DC sends Read-Req to home
a. PCPU issues read on bus
Directory entry in dirty so
DC forwards Read-Req to
dirty cluster
b. PCPU issues Sharing-Writeback
on bus.
DC updates directory state to shared
LOCAL
HOME
a. PCPU issues read on bus
Cache data sourced by dirty cache onto bus
DC sends Read-Rply to local
DC sends Sharing Writeback to home
1
2
Read-req
Read-req
3b
3a
Sh.-WB
Rd-Rply
REMOTE

## Slide 64: Read-Excl. to Shared Block
a.CPU’s write buffer issues RdX on bus
and is forced to retry
RAC entry is allocated
DC sends RdX Req to home
b.RC receives RdX reply w/ data and inv.
Count; releases CPU arbitration
Write-buffer repeats RdX and RAX responds
w/ data
Write-buffer retires write
c.RAC entry invalidate count is dec. with
each Inv.Ack
When 0, RAC is deallocated
PCPU issues rdX on bus to inv. Shared
copies
DC sends Inv.Ack to requesting cluster
a.PCPU issues rdX on bus
Directory entry is shared
DC sends Inv.Req to all
copies & RdX.Rply w/ data
and inv count to local
DC updates state to dirty
1
2a
2b
1:n
3
1:n
LOCAL
HOME
REMOTE

## Slide 65: Some issues
DASH Protocol : 3-hop
DIRNNB : 4-hop
DASH: A writer provides a read copy directly to the requestor (Also implemented in SGI Origin)
Also writes back the copy to home
Race between updating home and cacher!
Reduces 4-hop to 3-hop
Problematic

## Slide 66: Performance: Latencies
Local
  29 pcycles
Home
  100 pcycles
Remote
  130+ pcycles
Queuing delays
  +20% to 100%
Future Scaling?
  Integration
    latency reduced
  But CPU speeds increase
  Relative: no change

## Slide 67: Performance
Simulation for up to 64 procs
  Speedup over uniprocessors
    Sub-linear for 3 applications
  Marginal Efficiency:
    Utilization w/ n+1 procs/ Utilization w/ n procs
Actual Hardware: 16 procs
  Very close for one application
  Optimistic for others
  ME much better here

## Slide 68: SCI
IEEE Standard
Not a complete system
  Interfaces each node has to provide
Ring interconnect
Sharing list based
  Doubly linked list
Lower storage requirements in the abstract
  In practice: SCI is in the cache, hence SRAM vs. DRAM in DASH

## Slide 69: SCI, contd.
Efficiency:
write to block shared by N nodes
  detach from list
  interrogate memory for head of the list
  link as head
  invalidate previous head
  continue till no other node left
  2N + 6 transcactions
But, SCI has included optimizations
  Tree structures instead of linked lists
  Kiloprocessor extensions